## Slide 1
Instruction:
Data Selection:
  Selection sample data sets and corresponding buffer. Provide conc values
Simulatenous Bkg Sub & …
  Check the date sets to be fit, up to 5. Provide q-range to fit (qMin & qMax).
  Click “Fit Alpha, Beta….” to do simultaneous background subtraction, and zero-concentration extroplation
Merge Zero Conc: merge extroplated zero-conc data(low q) and high conc data (high q)
  qMerge: q value chosen to merge
  mBsub: the high conc data set (#1 default)
Guinier Extraploation and Pair Distance Distribuion Analysis
  Those requires ATSAS software package
  In “Settings”, “Set ATSAS/bin Path” first
  Call ATSAS functions to do Guinier fit and GNOW calculations. Can do outside of this matlab program after “Merge Zero Conc”.

## Slide 2
New functions highlighted in yellow (a-d)
a
b
c
d
One can choose more buffer files, which will be associated with same sample # , e.g., buffer#3 file is associated with sample #3 file.
The “Use for Rest” checkbox allows using a buffer file for the rest samples. Need select buffer file first, then check the box. For example, load buffer file for Buffer2 then check box of Buffer2 will make the Buffer2 file applies to Buffer2,3,4 &5.
After “Fit Alpha, Beta & conc Extrop”, “Save BackSubs” bottom will allow saving all backsub files with alpha, beta values recorded in the files.
“Conc Ratios” will display conc ratio
“Save MetaData” will save all parameters used in the data processing, including file names, data, alpha, beta and checkbox values, into a matlab file. These parameter can be loaded by “Load MetaData” for a late check.